## Slide 1
IIIT HYDERABAD · EMBEDDED SYSTEMS & WIRELESS LAB
Agentic Edge AI
for Smart Cities
An edge-native multi-agent SLM framework for cross-domain reasoning
TARGET PLATFORM
Qualcomm QIDK
Guided by Prof. Anuradha Vattem | TA Lokabhiram Chintada
Energy
Air Quality
Water
Weather
Occupancy

## Slide 2
THE PROBLEM
From isolated alerts to cross-domain reasoning
Smart-city infrastructure is monitored as separate silos
Energy
siloed
Air Quality
siloed
Water
siloed
Weather
siloed
Occupancy
siloed
Existing systems are threshold-based
Value crosses threshold → alert generated
Little or no explanation of why it happened
The real gap: cross-domain root-cause reasoning. Causes can span multiple infrastructure domains, and detecting these relationships is difficult.
Edge deployment adds hard constraints
Bounded
memory
Limited
compute
Low
power
Low
latency
Core question: Can a small local model reason across multiple sensor domains, in real time, directly on an edge device?
02

## Slide 3
MOTIVATION
Why edge agents? Smart-city systems are coupled
One action, three domains
HVAC
adjustment
Energy
consumption
Air
quality
Occupancy
comfort
A siloed system sees separate alerts — a cross-domain agent connects them.
Why process intelligence at the edge?
Cloud AI | Edge AI
Network latency | Low-latency local inference
Continuous sensor transmission | Data remains local
Connectivity dependency | Works without connectivity
Large models / higher compute | Small, efficient models
QIDK advantage
Its NPU enables efficient local inference, making on-device SLM reasoning practical.
Takeaway: because domains are physically coupled, reasoning about one requires context from the others — the motivation for a cross-domain agent architecture.
03

## Slide 4
MOTIVATING SCENARIO
What a threshold system sees vs. what an agent explains
Synthetic building-day trace — 13:00 to 15:00
13:00
Baseline load
13:45
Energy spikes vs. occupancy
14:15
Outdoor temp rises
15:00
HVAC/air-quality link
Traditional system
"Energy threshold exceeded."
Proposed system
"Energy increased disproportionately to occupancy, coinciding with HVAC/air-quality load — investigate ventilation."
Key idea: the objective is not merely detecting anomalies, but explaining cross-domain causes. (Data shown is synthetic and illustrative; real IoT traces will be used during evaluation.)
04

## Slide 5
SYSTEM DESIGN
System architecture: event-driven multi-agent reasoning
IoT Sensor Streams
Raw multi-domain data
Edge Stream Processing
Filter · aggregate · window
Local State + History
Compact summaries only
Anomaly Detection
Non-LLM · always-on trigger
Only the relevant context is forwarded when the trigger fires
SLM Orchestrator Coordinates domain agents & performs cross-domain reasoning
DOMAIN AGENTS
Energy
Air Quality
Water
Weather
Occupancy
OUTPUTS
Explanation
Real-time Alert
Recommendation
Conversational Interface
05

## Slide 6
DESIGN PRINCIPLES
Designing for bounded resources
1
Bounded Memory
Sliding windows / ring buffers for recent state
Compact statistics and trends
Avoid feeding complete historical data to the model
2
Event-Driven Inference
Invoke SLM reasoning only on an anomaly or a user query
Avoid inference on every sensor tick
3
Efficient On-Device Inference
Lightweight / quantized models
Qualcomm AI acceleration
NPU-based inference
OPTIMIZATION TARGET
Bounded memory + Low latency + Useful reasoning
These objectives inherently compete — managing this trade-off is a core systems challenge.
06

## Slide 7
SCOPE
Capabilities & scope
Committed Core
Historical context
Comparison and diagnosis using recent / compact history
Event-driven intelligence
Reason only when necessary
Conversational decision support
Explain anomalies and provide recommendations
Edge-efficient inference
Lightweight / quantized models + NPU acceleration
Exploratory Extensions
Digital twin
Edge mesh
Sensor-drift recalibration
Conflict resolution
Scope principle: validate the foundation first — extensions remain exploratory until the core system is proven.
07

## Slide 8
ROADMAP
A 5-phase roadmap from foundation to evaluation
1
Foundation
Core pipeline, sensor ingestion & state store
2
Multi-Agent Build-out
Domain agents implemented per infrastructure area
3
Cross-Domain Intelligence
Orchestrator reasoning across agents
4
Interface & Storage
Conversational UI & historical storage
5
Integration & Evaluation
End-to-end system benchmarking
Phases 1–3 · Core Validation
Committed target given the project timeline
Phases 4–5 · Stretch Goals
Interface / storage — timeline permitting
08

## Slide 9
EVALUATION
Evaluation: engineering → research
Compare three configurations under the same conditions
Rule-based System
Threshold logic, no learning
Single SLM
One model, all domains
Multi-Agent SLM
Orchestrator + domain agents (proposed)
Metrics
Anomaly / root-cause accuracy
Inference latency
Memory usage
Power consumption
Model size
Network usage
NPU utilization
Research claim to test
Does cross-domain multi-agent reasoning improve root-cause accuracy while maintaining acceptable latency and power cost?
09

## Slide 10
LITERATURE
Prior work & where it falls short
Multi-agent edge AI
Hybrid agentic-AI + multi-agent frameworks exist for smart manufacturing / prescriptive maintenance — similar architecture (LLM planner + edge SLM agents), different application domain.
Building intelligence
A 2026 zero-shot multi-agent framework for human-building interaction, validated on 200+ commercial buildings — cloud / programmatic-reasoning focused, not edge cross-infrastructure.
SmartBench (2026)
Benchmarks LLMs for smart-home anomaly detection. Even strong frontier models struggle with contextual anomalies.
Claude Sonnet 4.5 — Context-independent
66%
Claude Sonnet 4.5 — Context-dependent
58%
Root-cause multi-agent systems
Existing work (e.g. mABC, Flow-of-Action) targets cloud / IT operations and microservice logs rather than physical IoT sensors.
10

## Slide 11
THE CONTRIBUTION
The proposed research gap
We did not find prior work combining all three:
Strict edge / on-device SLM deployment
Cross-domain reasoning across infrastructure
Explicit rule-based vs. single vs. multi-agent comparison
THE
GAP
POSITIONING
Not simply "using agents for smart cities" — evaluating whether an edge-native multi-agent SLM architecture performs useful cross-domain root-cause reasoning under real resource constraints.
11

## Slide 12
DISCUSSION
Questions for the guide & TA
1
Research framing
Does rule-based vs. single-SLM vs. multi-agent-SLM provide a defensible contribution, or should the baseline / ablation differ?
2
Scope
Given the timeline, should Phases 1–3 be the committed target, with interface/storage as stretch goals?
3
QIDK deployment
What model sizes are realistically deployable on the QIDK NPU? Should this be benchmarked early rather than assumed?
4
Data
Are there existing multi-domain smart-building datasets to use, or is synthetic data + a small real pilot more appropriate?
5
Prior work
What prior multi-agent LLM/SLM work on cross-domain sensor reasoning should we check to avoid duplicating research?
Open floor
We welcome any further concerns or redirection before implementation begins.
12

## Slide 13
Thank You
Discussion & feedback welcome
Core question: Can a small local model reason across multiple sensor domains, in real time, directly on an edge device?
Guided by Prof. Anuradha Vattem | TA Lokabhiram Chintada
IIIT Hyderabad · Embedded Systems & Wireless Lab · Target platform: Qualcomm QIDK